## Slide 1: ECE 441 Single Bus Step Cycle Practice Questions

## Slide 2: Objective
Solve opcode and bus behavior when given instruction.

## Slide 4: Instruction Format
Single Effective Address Operation Word One word, specifies operation and mode
Special Operand Specifiers If any, one or two words
Immediate Operand or Source Effective Address Extension If any, one to six words
Destination Effective Address Extension If any, one to six words
*M68000 FAMILY PROGRAMMER’S REFERENCE MANUAL P2-1

## Slide 5: Effective Address
*MC68000 EDUCATIONAL COMPUTER BOARD USER’S MANUAL P4-16
Address modes | 
Dn | d8(An,Xn)
An | (xxx).W
(An) | (xxx).L
(An)+ | d16(PC)
-(An) | d8(PC,Xn)
d16(An) | #<data>

## Slide 6: Effective Address
00000000
00007FFF
00008000
FFFF7FFF
FFFF8000
FFFFFFFF
Absolute short (XXX).W 16bits
Absolute long (XXX).L 32bits
Absolute short (XXX).W 16bits
0000 0000 0000 0000 0000 0000 0000 0000 0000 0000 0000 0000 0111 1111 1111 1111
0000 0000 0000 0000 1000 0000 0000 0000 1111 1111 1111 1111 0111 1111 1111 1111
1111 1111 1111 1111 1000 0000 0000 0000 1111 1111 1111 1111 1111 1111 1111 1111
*MC68000 EDUCATIONAL COMPUTER BOARD USER’S MANUAL P4-20

## Slide 7: MOVE.L $7000,$B100
0 | 0 | Size | DESTINATION | SOURCE
0 | 0 | 1 0 | 0 0 1 1 1 1 | 1 1 1 0 0 0
Bus Cycle # | Address | Data |  |  |  |  |  |  | 
1 | A000 | 23F8 | 1 | 0 | 0 | 0 | 1 | 1 | 0
2 | A002 | 7000 | 1 | 0 | 0 | 0 | 1 | 1 | 0
3 | A004 | 0000 | 1 | 0 | 0 | 0 | 1 | 1 | 0
4 | A006 | B100 | 1 | 0 | 0 | 0 | 1 | 1 | 0
5 | 7000 | U | 1 | 0 | 0 | 0 | 1 | 0 | 1
6 | 7002 | U | 1 | 0 | 0 | 0 | 1 | 0 | 1
7 | B100 | U | 0 | 0 | 0 | 0 | 1 | 0 | 1
8 | B102 | U | 0 | 0 | 0 | 0 | 1 | 0 | 1
23F8 7000 0000B100

## Slide 8: LEA +5(A3),A2
0 | 1 | 0 | 0 | Register | 1 1 1 | Effective Address
Bus Cycle # | Address | Data |  |  |  |  |  |  | 
1 | A000 | 45EB | 1 | 0 | 0 | 0 | 1 | 1 | 0
2 | A002 | 0005 | 1 | 0 | 0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 0 | 0 1 0 | 1 1 1 | 1 0 1 0 1 1
45EB 0005

## Slide 9: MOVE.L (A1),(A2)
0 | 0 | Size | DESTINATION | SOURCE
0 | 0 | 1 0 | 0 1 0 0 1 0 | 0 1 0 0 0 1
Bus Cycle # | Address | Data |  |  |  |  |  |  | 
1 | A000 | 2491 | 1 | 0 | 0 | 0 | 1 | 1 | 0
2 | A100 | U | 1 | 0 | 0 | 0 | 1 | 0 | 1
3 | A102 | U | 1 | 0 | 0 | 0 | 1 | 0 | 1
4 | A200 | U | 0 | 0 | 0 | 0 | 1 | 0 | 1
5 | A202 | U | 0 | 0 | 0 | 0 | 1 | 0 | 1
2491

## Slide 10: CLR.L $A000
0 | 1 | 0 | 0 | 0 0 1 0 | Size | Effective Address
Bus Cycle # | Address | Data |  |  |  |  |  |  | 
1 | A000 | 42B9 | 1 | 0 | 0 | 0 | 1 | 1 | 0
2 | A002 | 0000 | 1 | 0 | 0 | 0 | 1 | 1 | 0
3 | A004 | A000 | 1 | 0 | 0 | 0 | 1 | 1 | 0
4 | A000 | 42B9 | 1 | 0 | 0 | 0 | 1 | 0 | 1
5 | A002 | 0000 | 1 | 0 | 0 | 0 | 1 | 0 | 1
6 | A002 | 0000 | 0 | 0 | 0 | 0 | 1 | 0 | 1
7 | A000 | 0000 | 0 | 0 | 0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 0 0 1 0 | 1 0 | 1 1 1 0 0 1
42B9 0000A000

## Slide 11: ROR (A2)+
1 | 1 | 1 | 0 | 0 | 1 | 1 | dr | 1 | 1 | Effective Address
Bus Cycle # | Address | Data |  |  |  |  |  |  | 
1 | A000 | E6DA | 1 | 0 | 0 | 0 | 1 | 1 | 0
2 | A200 | U | 1 | 0 | 0 | 0 | 1 | 0 | 1
1 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 1 | 1 | 0 1 1 0 1 0
3 | A200 | U | 0 | 0 | 0 | 0 | 1 | 0 | 1
E6DA

## Slide 12: PEA -15(A2)
0 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | Effective Address
Bus Cycle # | Address | Data |  |  |  |  |  |  | 
1 | A000 | 486A | 1 | 0 | 0 | 0 | 1 | 1 | 0
2 | A002 | FFF1 | 1 | 0 | 0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 1 0 1 0 1 0
3 | A6FE | A1F1 | 0 | 0 | 0 | 0 | 1 | 0 | 1
4 | A6FC | 0000 | 0 | 0 | 0 | 0 | 1 | 0 | 1
A2 → A200 -15 → FFF1 → FFFFFFF1
Calculates an effective address <ea> and pushes it onto the stack pointed to by address register A7 (the stack pointer, SP).
486A FFF1

## Slide 13: ADDI.L #$2,2(A2,A0)
0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | Size | Effective Address
Bus Cycle # | Address | Data |  |  |  |  |  |  | 
1 | A000 | 06B2 | 1 | 0 | 0 | 0 | 1 | 1 | 0
2 | A002 | 0000 | 1 | 0 | 0 | 0 | 1 | 1 | 0
3 | A004 | 0002 | 1 | 0 | 0 | 0 | 1 | 1 | 0
4 | A006 | 8002 | 1 | 0 | 0 | 0 | 1 | 1 | 0
5 | 4202 | U | 1 | 0 | 0 | 0 | 1 | 0 | 1
6 | 4204 | U | 1 | 0 | 0 | 0 | 1 | 0 | 1
7 | 4204 | U | 0 | 0 | 0 | 0 | 1 | 0 | 1
8 | 4202 | U | 0 | 0 | 0 | 0 | 1 | 0 | 1
0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 1 0 | 1 1 0 0 1 0
DISPLACEMENT : 1000 0000 XXXX XXXX (X: DISPLACEMENT INTEGER) => 1000 0010 (8002)
FFFFA000
A200
+ 2
4202
06B2 00000002 8002

## Slide 14: Understand Brief Extension Word
*M68000 FAMILY PROGRAMMER’S REFERENCE MANUAL P2-21
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
D/A | Register Number |  |  | W/L | 0 | 0 | 0 | Displacement Integer |  |  |  |  |  |  | 
D/A indicates the register used for indexing
  0 for data register
  1 for address register
W/L indicates the length for indexing (not operation)
  0 for word indexing
  1 for long indexing

## Slide 15: Understand Word and Long Indexing
*M68000 FAMILY PROGRAMMER’S REFERENCE MANUAL P2-10
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
D/A | Register Number |  |  | W/L | 0 | 0 | 0 | Displacement Integer |  |  |  |  |  |  | 
Word indexing allow 16 bits for destination operant with sign extension
Long indexing allow 32 bits for destination operant(when .L is specified)
Example |  | 
Instruction | ADDI.L #2, 2(A2,A0) | ADDI.L #2,2(A2,A0.L)
Opcode | 06B2 00000002 8002 | 06B2 00000002 8802
Destination Operant | $A200+$FFFFA000+2 = $4202 Only 16 bits preserved | $A200+$A000+2 = $14202 All 32 bits preserved

## Slide 16: BRA $3000
0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 8 BIT DISPLACEMENT
Bus Cycle # | Address | Data |  |  |  |  |  |  | 
1 | A000 | 6000 | 1 | 0 | 0 | 0 | 1 | 1 | 0
2 | A002 | 8FFE | 1 | 0 | 0 | 0 | 1 | 1 | 0
0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0000 0000
$A000 BRA $3000
$3000 XXXXXXX
$3000-$A002 = $8FFE
6000 8FFE

## Slide 18: MOVEM.L (A3)+,A0/D0
Register List Mask
Bus Cycle # | Address | Data |  |  |  |  |  |  | 
1 | A000 | 4CDB | 1 | 0 | 0 | 0 | 1 | 1 | 0
2 | A002 | 0101 | 1 | 0 | 0 | 0 | 1 | 1 | 0
3 | A300 | U | 1 | 0 | 0 | 0 | 1 | 0 | 1
4 | A302 | U | 1 | 0 | 0 | 0 | 1 | 0 | 1
5 | A304 | U | 1 | 0 | 0 | 0 | 1 | 0 | 1
6 | A306 | U | 1 | 0 | 0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1 | dr | 0 | 0 | 1 | Sz | Effective Address
0 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 1 1 0 1 1
Register List Mask
D0 | D1 | D2 | D3 | D4 | D5 | D6 | D7 | A0 | A1 | A2 | A3 | A4 | A5 | A6 | A7
A7 | A6 | A5 | A4 | A3 | A2 | A1 | A0 | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0
(A)+
-(A)
4CDB 0101